## Slide 1: Deep Neural Network and Accelerator Co-Design: Present and Future
  Sharc-lab @ Georgia Tech https://sharclab.ece.gatech.edu/
Cong (Callie) Hao
Assistant Professor
Georgia Institute of Technology
School of Electrical and Computer Engineering

## Slide 2: What is DNN and Accelerator Co-design?
Deep Neural Network (DNN) Design
Accelerator Design

## Slide 3: What is DNN and Accelerator Co-design?
Deep Neural Network (DNN) Design
Accelerator Design
DNN Model
Deploy the model to the device

## Slide 4: What is DNN and Accelerator Co-design?
Deep Neural Network (DNN) Design
Accelerator Design
Zoph, Barret, et at. "Learning transferable architectures for scalable image recognition." CVPR 2018
  An automatic neural architecture search (NAS) methodology – a.k.a. AutoML
  Boosts the quality and accuracy of machine learning algorithms
Chen Zhang, et al. “Optimizing fpga-based accelerator design for deep convolutional neural networks”, FPGA 2015
  On GPU/TPU/NPU: optimized (tuned) neural network implementations
  On FPGA: customized DNN accelerators

## Slide 5: What is DNN and Accelerator Co-design?
Deep Neural Network (DNN) Design
Accelerator Design
Zoph, Barret, et at. "Learning transferable architectures for scalable image recognition." CVPR 2018
  An automatic neural architecture search (NAS) methodology – a.k.a. AutoML
  Boosts the quality and accuracy of machine learning algorithms
Chen Zhang, et al. “Optimizing fpga-based accelerator design for deep convolutional neural networks”, FPGA 2015
  On GPU/TPU/NPU: optimized (tuned) neural network implementations
  On FPGA: customized DNN accelerators

## Slide 6: Three Levels of Co-Design in Cake Factory…
Bake a cake…
Build a plate…
Level 0
Oops cake too big

## Slide 7: Three Levels of Co-Design in Cake Factory…
Bake a cake…
Build a plate…
Level 0
Level 1
Oops cake too big
Plate is different from expected…

## Slide 8: Three Levels of Co-Design in Cake Factory…
Bake a cake…
Build a plate…
Level 0
Level 1
Level 2
Oops cake too big
Plate is different from expected…
Bake&build in pairs!

## Slide 9: Three Levels of Co-Design for DNN/Accelerator
Deep Neural Network (DNN) Design
Accelerator Design
Neural Architecture Search (NAS)
Accelerator Design
Pure NAS
Level 0

## Slide 10: Three Levels of Co-Design for DNN/Accelerator
Deep Neural Network (DNN) Design
Accelerator Design
Hardware-aware NAS
NAS with HW cost
Accelerator Evaluation
Searched DNN
Neural Architecture Search (NAS)
Accelerator Design
Accelerator Design
Pure NAS
Level 0
Level 1

## Slide 11: Three Levels of Co-Design for DNN/Accelerator
Deep Neural Network (DNN) Design
Accelerator Design
Hardware-aware NAS
NAS with HW cost
Accelerator Evaluation
Searched DNN
Accelerator Fine-tune
True DNN and Accelerator Co-Design
Searched DNN + Accelerator
DNN and Accelerator Co-Design
Neural Architecture Search (NAS)
Accelerator Design
Accelerator Design
[ ]
[ ]
[ ]
Pure NAS
Level 0
Level 1
Level 2

## Slide 12: Three Levels of Co-Design for DNN/Accelerator
Accelerator Design
Hardware-aware NAS
NAS with HW cost
Accelerator Evaluation
Searched DNN
Accelerator Fine-tune
True DNN and Accelerator Co-Design
Searched DNN + Accelerator
DNN and Accelerator Co-Design
Accelerator Design
[ ]
[ ]
[ ]
Level 1
Level 2
Deep Neural Network (DNN) Design

## Slide 13: Three Levels of Co-Design for DNN/Accelerator
Accelerator Design
Hardware-aware NAS
NAS with HW cost
Accelerator Evaluation
Searched DNN
Accelerator Fine-tune
True DNN and Accelerator Co-Design
Searched DNN + Accelerator
DNN and Accelerator Co-Design
Accelerator Design
[ ]
[ ]
[ ]
Level 1
Level 2
Deep Neural Network (DNN) Design
Fixed Accelerator
Accelerator design can also change

## Slide 14: Level 2 Co-Design for DNN/Accelerator
Accelerator Fine-tune
True DNN and Accelerator Co-Design
Searched DNN + Accelerator
DNN and Accelerator Co-Design
[ ]
[ ]
[ ]
Level 2
Accelerator design can also change
Our major focus

## Slide 15: Level 2 Co-Design for DNN/Accelerator
Accelerator Fine-tune
True DNN and Accelerator Co-Design
Searched DNN + Accelerator
DNN and Accelerator Co-Design
[ ]
[ ]
[ ]
Level 2
Our major focus
Software: Neural Architecture Search (NAS)
Hardware: Implementation Search
Accelerator design can also change

## Slide 16: Level 2 Co-Design for DNN/Accelerator
Accelerator Fine-tune
True DNN and Accelerator Co-Design
Searched DNN + Accelerator
DNN and Accelerator Co-Design
[ ]
[ ]
[ ]
Level 2
Our major focus
Software: Neural Architecture Search (NAS)
Hardware: Implementation Search
=
NAIS
Accelerator design can also change

## Slide 17: Why Co-Design?
Independent NAS and Implementation search
  Long iterative procedure: time consuming
  Hardware-unfriendly DNN models: sub-optimal solutions
1. Software: DNN Model Search (NAS)
Deployment
Application, QoS & QoR Target, etc.
Well designed DNN model
2. Hardware: Implementation Search
Independent NAS and implementation search

## Slide 18: NAIS: Simultaneous NAS + Implementation
Simultaneous NAS and Implementation search
DNN 1
IMP 1
DNN 2
IMP 2
DNN n
IMP n
…
…
Solution Pair 1
Solution Pair 2
Solution Pair 3
NAIS Engine

## Slide 19: NAIS: Simultaneous NAS + Implementation
Simultaneous NAS and Implementation search
“One-click AI"
Automated AI algorithm development and deployment
DNN 1
IMP 1
DNN 2
IMP 2
DNN n
IMP n
…
…
Solution Pair 1
Solution Pair 2
Solution Pair 3
NAIS Engine
“Good AI”
Bridge the gap between SW/HW for higher quality solutions

## Slide 20: Key Methodologies for Co-Design
Software:
Neural Architecture Search Space
Hardware:
Implementation Search Space

## Slide 21: Key Methodologies for Co-Design
Software:
Neural Architecture Search Space
Hardware:
Implementation Search Space
Method 1: find something in the middle and connect to both SW and HW
FPGA/DNN Co-Design [DAC’19, SysML’20]
1

## Slide 22: Key Methodologies for Co-Design
Software:
Neural Architecture Search Space
Hardware:
Implementation Search Space
Method 1: find something in the middle and connect to both SW and HW
Method 2: merge the two spaces – formulate both in one equation
FPGA/DNN Co-Design [DAC’19, SysML’20]
A True NAIS work
EDD [ICCAD’19, DAC’20]
1
2

## Slide 23: Key Methodologies for Co-Design
Software:
Neural Architecture Search Space
Hardware:
Implementation Search Space
Method 1: find something in the middle and connect to both SW and HW
FPGA/DNN Co-Design [DAC’19, SysML’20]
1
Hao, Cong, Xiaofan Zhang, Yuhong Li, Sitao Huang, Jinjun Xiong, Kyle Rupnow, Wen-mei Hwu, and Deming Chen. "FPGA/DNN co-design: An efficient design methodology for IoT intelligence on the edge." ACM/IEEE DAC, 2019. (seems to be most cited in DAC 2019)

## Slide 24: FPGA/DNN Co-Design
  DNNs
  Accelerators (FPGA)

## Slide 25: FPGA/DNN Co-Design
  DNNs are usually built by repeated or similar basic blocks
https://d2l.ai/chapter_convolutional-modern/resnet.html
  Accelerators (FPGA)

## Slide 26: FPGA/DNN Co-Design
  DNNs are usually built by repeated or similar basic blocks
https://d2l.ai/chapter_convolutional-modern/resnet.html
  Accelerators (FPGA) are usually built by Processing Elements (PE)
Convolution
1x1
Convolution
3x3
Pooling
Relu
Depth-wise Convolution
3x3

## Slide 27: FPGA/DNN Co-Design
  DNNs are usually built by repeated or similar basic blocks
https://d2l.ai/chapter_convolutional-modern/resnet.html
  Accelerators (FPGA) are usually built by Processing Elements (PE)
Convolution
1x1
Convolution
3x3
Pooling
Relu
Depth-wise Convolution
3x3
PE implements basic blocks
– “something in the middle” we are looking for

## Slide 28: FPGA/DNN Co-Design
determines
determines
Software
Hardware
Basic Building Block
DNN
FPGA

## Slide 29: FPGA/DNN Co-Design
Software
Hardware
DNN
FPGA
Conv 3x3
Conv 1x1
DW-Conv 3x3
Activation
Conv 3x3
Conv 1x1
DW-Conv 3x3
Activation
Input
Output
…
2nd Basic Block
1st Basic Block
3rd Basic Block

## Slide 30: FPGA/DNN Co-Design
Software
Hardware
DNN
FPGA
Conv 3x3
Conv 1x1
DW-Conv 3x3
Activation
Conv 3x3
Conv 1x1
DW-Conv 3x3
Activation
Input
Output
…
2nd Basic Block
1st Basic Block
3rd Basic Block
Convolution
1x1
Convolution
3x3
Pooling
Relu
Depth-wise Convolution 3x3
Implements

## Slide 31: FPGA/DNN Co-Design
Software
Hardware
DNN
FPGA
Conv 3x3
Conv 1x1
DW-Conv 3x3
Activation
How to choose these basic building blocks from a large design space?

## Slide 32: DNN/FPGA Co-Design Flow
Target ML task; FPGA device (resources); performance targets (QoS)
Auto-HLS:
FPGA Accelerator Generator
Step 1. Basic building block modeling
Step 2. Building block selection
Step 3. DNN search and update
Auto-DNN: Co-Search Engine
Software: DNN Model
Hardware: FPGA Accelerator

## Slide 33: DNN/FPGA Co-Design Flow
Target ML task; FPGA device (resources); performance targets (QoS)
Auto-HLS:
FPGA Accelerator Generator
Step 1. Basic building block modeling
Step 2. Building block selection
Step 3. DNN search and update
Auto-DNN: Co-Search Engine
Software: DNN Model
Hardware: FPGA Accelerator
1
2
3
4
Input feature maps:
8x8 tiling
Load data
CONV 3x3
CONV 1x1
Pooling
Write back
Time
1
1
1
1
1
2
2
2
2
2
3
3
3
3
3
4
4
4
4
4
Off-chip data transfer
IP outputs
Accelerator template

## Slide 34: DNN/FPGA Co-Design Flow
Auto-HLS:
FPGA Accelerator Generator
Step 1. Basic building block modeling
Step 2. Building block selection
Step 3. DNN search and update
Auto-DNN: Co-Search Engine
Software: DNN Model
Hardware: FPGA Accelerator

## Slide 35: DNN/FPGA Co-Design Flow
Auto-HLS:
FPGA Accelerator Generator
Step 1. Basic building block modeling
Step 2. Building block selection
Step 3. DNN search and update
Auto-DNN: Co-Search Engine
Software: DNN Model
Hardware: FPGA Accelerator
CV screening
Phone Interview
Onsite Interview
Job interview…

## Slide 36: DNN/FPGA Co-Design Flow
Auto-HLS:
FPGA Accelerator Generator
Step 1. Basic building block modeling
Step 2. Building block selection
Step 3. DNN search and update
Auto-DNN: Co-Search Engine
Software: DNN Model
Hardware: FPGA Accelerator
To provide performance estimation of a DNN

## Slide 37: DNN/FPGA Co-Design Flow
Auto-HLS:
FPGA Accelerator Generator
Step 1. Basic building block modeling
Step 2. Building block selection
Step 3. DNN search and update
Auto-DNN: Co-Search Engine
Software: DNN Model
Hardware: FPGA Accelerator
Only Keep promising ones to reduces design space

## Slide 38: DNN/FPGA Co-Design Flow
Auto-HLS:
FPGA Accelerator Generator
Step 1. Basic building block modeling
Step 2. Building block selection
Step 3. DNN search and update
Auto-DNN: Co-Search Engine
Software: DNN Model
Hardware: FPGA Accelerator
Only Keep promising ones to reduces design space
0.54
PF=16
PF=8
PF=4
0.57
0.55
0.53
0.52
0.51
Building Blocks
Pareto Curves
0.56
Accuracy (IoU)

## Slide 39: DNN/FPGA Co-Design Flow
Auto-HLS:
FPGA Accelerator Generator
Step 1. Basic building block modeling
Step 2. Building block selection
Step 3. DNN search and update
Auto-DNN: Co-Search Engine
Software: DNN Model
Hardware: FPGA Accelerator
Perturb, train, and select DNNs within performance constraint

## Slide 40: NAIS Victory – DAC System Design Contest
Design Automation Conference System Design Contest (DAC-SDC)
  Object detection on FPGA/GPU
Our Achievements
  2018: Third place @ FPGA (3 out of 51)

## Slide 41: NAIS Victory – DAC System Design Contest
Design Automation Conference System Design Contest (DAC-SDC)
  Object detection on FPGA/GPU
Our Achievements
  2018: Third place @ FPGA (3 out of 51)
Independently designed DNN and FPGA accelerator – a lot of iterations!

## Slide 42: NAIS Victory – DAC System Design Contest
Design Automation Conference System Design Contest (DAC-SDC)
  Object detection on FPGA/GPU
Our Achievements
  2018: Third place @ FPGA (3 out of 51)
  2019: Double championship @ FPGA and GPU (1 out of 58, 1 out of 56)
Independently designed DNN and FPGA accelerator – a lot of iterations!

## Slide 43: NAIS Victory – DAC System Design Contest
Design Automation Conference System Design Contest (DAC-SDC)
  Object detection on FPGA/GPU
Our Achievements
  2018: Third place @ FPGA (3 out of 51)
  2019: Double championship @ FPGA and GPU (1 out of 58, 1 out of 56)
Independently designed DNN and FPGA accelerator – a lot of iterations!
NAIS co-design leads to victory!

## Slide 44: NAIS Victory – DAC System Design Contest
Media coverage and open-source code
2020: https://github.com/jgoeders/dac_sdc_2020_designs
2019: https://github.com/TomG008/SkyNet
2018: https://github.com/onioncc/iSmartDNN
https://www.ibm.com/blogs/research/2019/06/winning-ai-algorithms-drones/

## Slide 45: Key Methodologies for Co-Design
Software:
Neural Architecture Search Space
Hardware:
Implementation Search Space
Method 1: find something in the middle and connect to both SW and HW
FPGA/DNN Co-Design [DAC’19, SysML’20]
1

## Slide 46: Key Methodologies for Co-Design
Software:
Neural Architecture Search Space
Hardware:
Implementation Search Space
Method 2: merge the two spaces – formulate both in one equation
A True NAIS work
EDD [ICCAD’19, DAC’20]
2
Li, Yuhong, Cong Hao, Xiaofan Zhang, Xinheng Liu, Yao Chen, Jinjun Xiong, Wen-mei Hwu, and Deming Chen. "EDD: Efficient differentiable DNN architecture and implementation co-search for embedded AI solutions." DAC 2020

## Slide 47: Key Methodologies for Co-Design
Software:
Neural Architecture Search Space
Hardware:
Implementation Search Space
Method 2: merge the two spaces – formulate both in one equation
A True NAIS work
EDD [ICCAD’19, DAC’20]
2
  Put {A, I} into one formulation, preferably differentiable
  Solve {A, I} using continuous optimization, e.g., Gradient Descent
{A}
{I}

## Slide 48: NAIS Formulation
  Implementation is fixed (not in the search space)
  Implementation is also variable
  is differentiable with respect to
  is differentiable with respect to
  Consider resource constraints
Existing Formulation
NAIS Formulation
  Hardware-ware NAS
  True co-design

## Slide 49: NAIS Formulation
  Implementation is fixed (not in the search space)
  Implementation is also variable
  is differentiable with respect to
  is differentiable with respect to
  Consider resource constraints
How to formulate as differentiable with respect to ?
Challenge
Existing Formulation
NAIS Formulation
  Hardware-ware NAS
  True co-design

## Slide 50: Differentiable DNN Architecture Search
…
-
…
DNN
One candidate operation
Candidate operations of
Neural Architecture Search (NAS)
…
…

## Slide 51: Differentiable DNN Architecture Search
…
-
…
DNN
One candidate operation
Candidate operations of
Neural Architecture Search (NAS)
…
…
Discrete solution space

## Slide 52: Differentiable DNN Architecture Search
…
-
…
DNN
One candidate operation
Candidate operations of
Neural Architecture Search (NAS)
…
…
Sampling parameter
Operations sampled following Gumbel-Softmax distribution
is differentiable with respect to
From discrete to continuous for differentiable:
Gumbel-Softmax

## Slide 53: Differentiable Implementation Search
One candidate operation
NAS
…
Quantization of
Implementation Search
-bit
-bit
-bit
-

## Slide 54: Differentiable Implementation Search
One candidate operation
NAS
…
Quantization of
Implementation Search
-bit
-bit
-bit
-
Similar technique:
Gumbel-Softmax

## Slide 55: Differentiable Implementation Search
One candidate operation
NAS
…
Quantization of
Implementation Search
-bit
-bit
-bit
-
Similar technique:
Gumbel-Softmax
: other implementation variables

## Slide 56: Now Since Everything is Differentiable…
One candidate operation
NAS
…
Quantization of
Implementation Search
-bit
-bit
-bit
-
Similar technique:
Gumbel-Softmax
: other implementation variables
Differentiable
Differentiable
Continuous Optimization: gradient descent

## Slide 57: Comparisons with hardware-aware NAS
GPU-oriented DNN
FPGA-oriented DNN

## Slide 58: Comparisons with hardware-aware NAS
EDD-Net-1: targets GPU
EDD-Net-2: targets recursive FPGA accelerator
EDD-Net-3: targets pipelined FPGA accelerator

## Slide 59: Follow-up Works using Differentiable Approach

## Slide 60: What’s NAIS’s Next?
Software: Neural Architecture Search (NAS)
Hardware: Implementation Search
=
NAIS

## Slide 61: What’s NAIS’s Next?
Software: Neural Architecture Search (NAS)
Hardware: Implementation Search
=
NAIS

## Slide 62: What’s NAIS’s Next?
Software: Neural Architecture Search (NAS)
Hardware: Implementation Search
=
NAIS
Multi-modal Multi-task Models

## Slide 63: What’s NAIS’s Next?
Software: Neural Architecture Search (NAS)
Hardware: Implementation Search
=
NAIS
Heterogeneous Platform Mapping-aware NAIS
Multi-modal Multi-task Models

## Slide 64: Multi-modal Multi-Task Models (MMMT)
Multi-modal: process and relate information from multiple modalities
  Text: natural language
  Visual: images or videos
  Vocal: sounds
  Point clouds, sensor data (accelerometer, speed), etc.
Huang Z, et al. Multi-modal sensor fusion-based deep neural network for end-to-end autonomous driving with scene understanding. IEEE Sensors Journal. 2020 Jun 17.
Nobis, Felix, et al. "A deep learning-based radar and camera sensor fusion architecture for object detection." 2019 Sensor Data Fusion: Trends, Solutions, Applications (SDF). IEEE, 2019.
Yang, Zhengyuan, et al. "End-to-end multi-modal multi-task vehicle control for self-driving cars with visual perceptions." 2018 24th International Conference on Pattern Recognition (ICPR). IEEE, 2018.

## Slide 65: Multi-modal Multi-Task Models (MMMT)
Multi-modal: process and relate information from multiple modalities
  Text, visual, vocal, motion, etc.
Sound
Image
Motion

## Slide 66: Multi-modal Multi-Task Models (MMMT)
Multi-modal: process and relate information from multiple modalities
  Text, visual, vocal, motion, etc.
Multi-task: to learn multiple related tasks jointly
  Knowledge transfer
  Improve the generalization performance
  Mitigate training (labeled) data sparsity
Ruder, Sebastian. "An overview of multi-task learning in deep neural networks." arXiv preprint arXiv:1706.05098 (2017).

## Slide 67: Multi-modal Multi-Task Models (MMMT)
Multi-modal: process and relate information from multiple modalities
  Text, visual, vocal, motion, etc.
Multi-task: to learn multiple related tasks jointly
  Knowledge transfer
  Improve the generalization performance
  Mitigate training (labeled) data sparsity
Largely increased complexity in model structure

## Slide 68: Heterogeneous Platforms
https://www.xilinx.com/support/documentation/white_papers/wp505-versal-acap.pdf
Talpes, Emil, et al. "Compute solution for tesla's full self-driving computer." IEEE Micro 40, no. 2 (2020): 25-35.

## Slide 69: Heterogeneous Platforms
https://www.xilinx.com/support/documentation/white_papers/wp505-versal-acap.pdf
Talpes, Emil, et al. "Compute solution for tesla's full self-driving computer." IEEE Micro 40, no. 2 (2020): 25-35.
Largely increased complexity in heterogeneous platforms

## Slide 70: When MMMT Meets Heterogeneity
Largely increased complexity in model structure
Largely increased complexity in heterogeneous platforms
Mapping starts to matter…
Scheduling starts to matter…
Optimization on each device also matters…

## Slide 71: When MMMT Meets Heterogeneity
Largely increased complexity in model structure
Largely increased complexity in heterogeneous platforms
Mapping starts to matter…
Scheduling starts to matter…
Optimization on each device also matters…
NAIS
Mapping Formulation
Scheduling Formulation
…

## Slide 72: An Example of NAIS + Mapping Formulation
Network on Chip
ACC1
ACC2
Shared Buffer
ACC3
ACC4
Shared Buffer
0.7
0.2
0.1
0.2
0.1
0.5
0.2
NAIS
Mapping Formulation
Hao, Cong, and Deming Chen. "Software/Hardware Co-design for Multi-modal Multi-task Learning in Autonomous Systems." In 2021 IEEE 3rd AICAS, 2021.

## Slide 73: NAIS + Scheduling + Mapping
NAIS
Mapping
Xinyi, Zhang, Cong Hao, et al., “H2H: Heterogeneous Model to Heterogeneous System Mapping with Computation and Communication Awareness” To appear at DAC’22
Scheduling

## Slide 74: NAIS + MMMT + Heterogeneity
NAIS
Mapping
Scheduling
Implementation Optimization
Hao, Cong, and Deming Chen. "Software/Hardware Co-design for Multi-modal Multi-task Learning in Autonomous Systems." IEEE 3rd AICAS, 2021.
Xinyi, Zhang, Cong Hao, et al., “H2H: Heterogeneous Model to Heterogeneous System Mapping with Computation and Communication Awareness” To appear at DAC’22
Li, Yuhong, Cong Hao, et al. "EDD: Efficient differentiable dnn architecture and implementation co-search for embedded ai solutions." ACM/IEEE DAC, 2020

## Slide 75: Summary & Thanks!
Basic: DNN and Accelerator Co-design – three levels
NAIS: simultaneous neural architecture and implementation co-search
Future: when multi-modal multi-task (MMMT) models meet heterogeneous platforms
Contact:
callie.hao@ece.gatech.edu
Sharc-lab @ Georgia Tech (https://sharclab.ece.gatech.edu/)
NAIS