## Slide 1: Smart Reconfigurable Computing for GNNs and Transformers
Cong (Callie) Hao
Assistant Professor
Georgia Institute of Technology
School of Electrical and Computer Engineering
Sharc-lab @ Georgia Tech https://sharclab.ece.gatech.edu/
ROAD4NN workshop @ DAC’23

## Slide 2: Self-Introduction
Cong (Callie) Hao
  Assistant Professor at Georgia Tech ECE
  Faculty Fellow at GT (2021~2022)
  Postdoc at UIUC (2018~2020)
  Ph.D. in Japan, Waseda University (2017)
  Email: callie.hao@ece.gatech.edu
  Homepage: http://callie.ece.gatech.edu

## Slide 3: Self-Introduction
Sharc Lab
Software/Hardware Co-Design for Intelligence and Efficiency

## Slide 4: Our ROAD4NN
Architectures
EDA Tools
LightningSim: Fast and Accurate Trace-Based Simulation for High-Level Synthesis
FlowGNN: A generic Graph Neural Network (GNN) accelerator on FPGA
GNNBuilder: An automated GNN accelerator generator
Edge-MoE: Multi-task Vision Transformer (HW)
DGNN-Booster: A Generic FPGA Accelerator Framework For Dynamic Graph Neural Network Inference
INR-Arch: A Dataflow Architecture and Compiler for Arbitrary-Order Gradient Computations

## Slide 5: Our ROAD4NN
FlowGNN: A generic Graph Neural Network (GNN) accelerator on FPGA
  HPCA’23
  Written in Vitis HLS
  Open-source
  In collaboration with High Energy Physicists
Architectures
EDA Tools
Rishov Sarkar
[image source] https://www.quantamagazine.org/growing-anomalies-at-the-large-hadron-collider-hint-at-new-particles-20200526/
The first general GNN architecture with on-FPGA verification

## Slide 6: Our ROAD4NN
GNNBuilder: An automated GNN accelerator generator
  FPL’23
  Open-source
  From Standard PyTorch
Architectures
EDA Tools
Stefan Abi-Karam
The first automated GNN accelerator generator from standard PyTorch

## Slide 7: Our ROAD4NN
Architectures
EDA Tools
Edge-MoE: Multi-task Vision Transformer (HW)
UT Austin Team
Rishov Sarkar
The first multi-task learning with dynamic task-level sparsity!
  Under review
  Written in Vitis HLS
  Open-source

## Slide 8: Our ROAD4NN
LightningSim: Fast and Accurate Trace-Based Simulation for High-Level Synthesis
Architectures
EDA Tools
  FCCM’23
  Best Paper Runner-up
  Open-source
The first HLS simulator with RTL-like accuracy and C-like speed
Rishov Sarkar
HLS Synthesis
LightningSim⚡
IR Trace Generation
❶
IR Trace Analysis
❷
(A) Make LLVM IR executable
Execute modified IR and dump a trace
(B) Make LLVM IR traceable
(C) Trace parsing
Non-pipelined non-dataflow basic blocks
Dataflow basic blocks
(D) Resolving dynamic schedule
(E) Calculating stalls
(F) Modeling AXI interfaces
LLVM IR
bitcode
Static
scheduling
information
Change
FIFO depth
Re-compute stalls
without re-simulating
(unlike current HLS
or simulation tools)
Dumped Trace

## Slide 9: FlowGNN – A generic GNN architecture
LightningSim: Fast and Accurate Trace-Based Simulation for High-Level Synthesis
FlowGNN: A generic Graph Neural Network (GNN) accelerator on FPGA
GNNBuilder: An automated GNN accelerator generator
Architectures
EDA Tools
Edge-MoE: Multi-task Vision Transformer (HW)
DGNN-Booster: A Generic FPGA Accelerator Framework For Dynamic Graph Neural Network Inference
INR-Arch: A Dataflow Architecture and Compiler for Arbitrary-Order Gradient Computations

## Slide 10: What are Graph Neural Networks (GNNs)?
[Slide credit: Structured deep models: Deep learning on graphs and beyond]

## Slide 11: What are Graph Neural Networks (GNNs)?
[Slide credit: Structured deep models: Deep learning on graphs and beyond]

## Slide 12: What are Graph Neural Networks (GNNs)?
[Slide credit: Structured deep models: Deep learning on graphs and beyond]
❷ Aggregate incoming messages for each node
❶ Send messages along all edges based on node and edge embeddings
❸ Transform each node embedding using aggregated messages to get next layer node embedding
Message Passing
Node Transformation

## Slide 13: Real-time GNN Inference
[image source] Shi, Weijing, and Raj Rajkumar. "Point-gnn: Graph neural network for 3d object detection in a point cloud.“ CVPR 2020
[image source] https://www.quantamagazine.org/growing-anomalies-at-the-large-hadron-collider-hint-at-new-particles-20200526/
Real-time Inference is required:
  LiDAR and Point Cloud Data for Autonomous Driving
  High Energy Physics
  Fraud and spam detection
Sometimes nanosecond latency

## Slide 14: Existing Work
Most focus on Graph Convolution Network (GCN): A limited type
Heavy pre-processing: Not suitable for real-time
Most on ASIC via simulation: not end-to-end, far from practical

## Slide 15: Existing Work vs. Ours
Support a wide range of GNNs: Generic
No pre-processing: Real-time oriented
Evaluated end-to-end on FPGA
Most focus on Graph Convolution Network (GCN): A limited type
Heavy pre-processing: Not suitable for real-time
Most on ASIC via simulation: not end-to-end, far from practical
FlowGNN: a dataflow-based architecture (HPCA’23)
High-Level Synthesis (HLS) based
Open sourced: https://github.com/sharc-lab/flowgnn

## Slide 16: Message Passing in GNNs
GNN at layer
: Edge Embedding
: Node Embedding
: Aggregated Message
: Edge Embedding
: Node Embedding
Aggregation
Message Transformation
Node Transformation
Update
Msg.
Buffer
2/1
Size:
O(N)
Msg.
Buffer
1/2
Size:
O(N)
Message Passing (Scatter)
Message Passing (Gather)
Node Transformation (NT)
GNN at layer

## Slide 17: Message Passing in GNNs
GNN at layer
: Edge Embedding
: Node Embedding
: Aggregated Message
: Edge Embedding
: Node Embedding
Aggregation
Message Transformation
Node Transformation
Update
Msg.
Buffer
2/1
Size:
O(N)
Msg.
Buffer
1/2
Size:
O(N)
GNN at layer
Message Passing (Scatter)
Message Passing (Gather)
Node Transformation (NT)
Node Transformation (NT)
•
Multi
-
layer Perceptron
•
Activation
•
Self
-
attention
Edge Embedding (EE)
+ Message Passing (MP)
+
Node
𝒏
𝟏
’s
embedding
+
+
Edge
(
𝒏
𝟏
,
𝒏
𝟐
)
’s embedding
Edge
(
𝒏
𝟏
,
𝒏
𝟑
)
’s embedding
Edge
(
𝒏
𝟏
,
𝒏
𝟒
)
’s embedding
Sequentially

## Slide 18: Architecture to Support Message Passing

## Slide 19: Architecture to Support Message Passing

## Slide 20: Pipelining Strategies
NT
MP
(a) Non-pipeline
MP
1
2
3
4
NT
(c) Baseline dataflow pipeline
Node queue for message passing
1
3
2
4
1
2
3
4
1
3
2
NT
MP
(b) Fixed pipeline
4
Idle time because of imbalanced NT and MP
NT: Node Transformation
MP: Message Passing

## Slide 21: Pipelining Strategies
MP
1
2
3
4
NT
(c) Baseline dataflow pipeline
Node queue for message passing
1
3
2
4
Can we do better?
How can we NOT sacrifice performance for generality?
Drawback: no node/edge level parallelism: one by one is too slow!

## Slide 22
MP
1
2
3
4
NT
(c) Baseline dataflow pipeline
Node queue for message passing
1
3
2
4
MP1
1
2
3
4
NT1
(d) FlowGNN pipeline with multiple NT/MP
NT2
MP2
MP3
MP4

## Slide 23: FlowGNN pipeline with node/edge parallelism
MP1
1
2
3
4
NT1
(d) FlowGNN pipeline with multiple NT/MP
NT2
MP2
MP3
MP4

## Slide 24: FlowGNN pipeline with node/edge parallelism
MP1
1
2
3
4
NT1
(d) FlowGNN pipeline with multiple NT/MP
NT2
MP2
MP3
MP4
MP1
MP2
Challenge: how to avoid bank conflicts?
1
2
3
MP1 and MP2 must both write to this node!

## Slide 25: FlowGNN pipeline with node/edge parallelism
MP1
1
2
3
4
NT1
NT2
MP2
MP3
MP4
MP1
MP2
Challenge: how to avoid bank conflicts?
1
2
3
MP1 and MP2 must both write to this node!
MP3
Solution: each MP unit is responsible for a unique set of destination nodes
1
2
3
Notes: We can make each MP unit responsible for its own set of destination nodes and have it process all its incoming edges. This way, no two MP units will have to write to the same memory bank.

## Slide 26: FlowGNN pipeline with node/edge parallelism
MP1
MP2
Challenge: how to avoid bank conflicts?
1
2
3
MP1 and MP2 must both write to this node!
MP3
Solution: each MP unit is responsible for a unique set of destination nodes
1
2
3
Challenge: how to stream nodes from multi-NT to multi-MP?
NT1
NT2
MP2
MP3
MP1
MP4
Notes: But now we can’t have a simple node queue anymore. How can we stream nodes from multiple NT units to multiple MP units, keeping in mind the destination node scheme I just mentioned?

## Slide 27: FlowGNN pipeline with node/edge parallelism
MP1
MP2
Challenge: how to avoid bank conflicts?
1
2
3
MP1 and MP2 must both write to this node!
MP3
Solution: each MP unit is responsible for a unique set of destination nodes
1
2
3
Challenge: how to stream nodes from multi-NT to multi-MP?
NT1
NT2
MP2
MP3
MP1
MP4
Solution: multi-queue multicasting NT-to-MP adapter
NT1
NT2
MP2
MP3
MP1
MP4
Q
Q
Q
Q
Q
Q
NT to MP
Notes: That’s where the multi-queue multicasting NT-to-MP adapter comes in. This thing will take one queue from each NT unit and distribute node data to separate queues for each MP unit.

## Slide 28: FlowGNN pipeline with node/edge parallelism
Challenge: how to stream nodes from multi-NT to multi-MP?
NT1
NT2
MP2
MP3
MP1
MP4
Solution: multi-queue multicasting NT-to-MP adapter
NT1
NT2
MP2
MP3
MP1
MP4
Q
Q
Q
Q
Q
Q
NT to MP
MP1
1
2
3
4
NT1
Multi-queue multicasting adapter
MP1’s destination nodes
NT2
MP2
MP3
MP4
MP2’s destination nodes
MP3’s destination nodes
MP4’s destination nodes

## Slide 29: FlowGNN: Parallelized Architecture
Notes: So now we can see the full FlowGNN architecture, with multiple node transformation units and multiple message passing units, all working in parallel.

## Slide 30: Experiment Setup
Evaluated on six GNN models
Notes: We evaluate FlowGNN on six models, which are each representative of a family of GNNs. For instance, GAT represents the family of GNNs with anisotropic message passing, and PNA represents GNNs using multiple aggregation methods.

## Slide 31: Experiment Setup
Evaluated end-to-end on-board on Xilinx Alveo U50 @ 300 MHz
  CPU baseline: Intel Xeon Gold 6226R (batch size 1)
  GPU baseline: NVIDIA RTX A6000 (batch size 1 ~ 1024)
Evaluated on seven datasets, including one from High-Energy Physics
Notes: We evaluate our framework end-to-end on the Xilinx Alveo U50 Acceleration Board, targeting a 300 MHz clock frequency.
We compare against the CPU and GPU baselines shown, and we use seven datasets: two molecular datasets of lots of thousands of small graphs, four larger single graph datasets, and one dataset of 10,000 graphs from High-Energy Physics.

## Slide 32: Evaluation – End-to-end Latency
(
a
)
M
o
l
H
I
V
GIN
FlowGNN: 0.05ms
On GPU: batch size from 1 to 1024
Notes: Here we show comparisons on our molecular datasets against GPU and CPU baselines. We see that FlowGNN achieves 50 to 250 times speedup over CPU and 50 to 480 times speedup over GPU at batch size one.
Although batch size 1 is the only fair comparison in a real-time setting, we also compare against GPU at higher batch sizes, and we still see speedup on all models and both datasets up to batch size 64.
The FlowGNN GAT and DGN models even beat GPU at batch size 1024.

## Slide 33: Evaluation – End-to-end Latency
Notes: Here we show comparisons on our molecular datasets against GPU and CPU baselines. We see that FlowGNN achieves 50 to 250 times speedup over CPU and 50 to 480 times speedup over GPU at batch size one.
Although batch size 1 is the only fair comparison in a real-time setting, we also compare against GPU at higher batch sizes, and we still see speedup on all models and both datasets up to batch size 64.
The FlowGNN GAT and DGN models even beat GPU at batch size 1024.

## Slide 34: Evaluation – End-to-end Latency
Observations:
FlowGNN is 50~250x over CPU, 50~480x over GPU at bs=1
For all models, FlowGNN outperform GPU for bs<=64
For GAT and DGN, FlowGNN beats GPU at bs=1024
Notes: Here we show comparisons on our molecular datasets against GPU and CPU baselines. We see that FlowGNN achieves 50 to 250 times speedup over CPU and 50 to 480 times speedup over GPU at batch size one.
Although batch size 1 is the only fair comparison in a real-time setting, we also compare against GPU at higher batch sizes, and we still see speedup on all models and both datasets up to batch size 64.
The FlowGNN GAT and DGN models even beat GPU at batch size 1024.

## Slide 35: Design Space Exploration
Four reconfigurable parameters
  # of nodes in parallel: Pnode
  # of edges in parallel: Pedge
  # of elements in NT: Papply
  # of elements in MP: Pscatter
Speedup is non-linear with respect to different parallelism factors
  An increase in one parameter does not guarantee speedup
  Future work
Notes: We also do a preliminary design space exploration to look at how changing parallelism factors changes the latency. We found that the parallelism factors have a non-linear and entangled effect, where sometimes increasing one parameter doesn’t necessarily change the latency whereas changing a different parameter does.

## Slide 36: GNNBuilder – An automated GNN builder
LightningSim: Fast and Accurate Trace-Based Simulation for High-Level Synthesis
FlowGNN: A generic Graph Neural Network (GNN) accelerator on FPGA
GNNBuilder: An automated GNN accelerator generator
Architectures
EDA Tools
Edge-MoE: Multi-task Vision Transformer (HW)
DGNN-Booster: A Generic FPGA Accelerator Framework For Dynamic Graph Neural Network Inference
INR-Arch: A Dataflow Architecture and Compiler for Arbitrary-Order Gradient Computations

## Slide 37: GNN Builder Workflow
A fully-automated, end-to-end GNN accelerator generation on FPGA
  Standard PyTorch input, FPGA bitstream + hostcode output

## Slide 38: GNN Builder Features
Generic: Wide range of GNN model types (follows FlowGNN principle)
Flexible: Highly customizable GNN models
Standard and Extensible API: Standard PyTorch as inputs
Completeness: Multi-level tasks (node, link, graph) with end-to-end workflow
DSE: Accelerator design space exploration (DSE) and optimization
Deployment: End-to-end with host code
Performance: Better than CPU and GPU

## Slide 39: Feature 1 – Generic
General / Sparse Matrix Multiplication (SpMM) is NOT all we need!
Supported GNNs:
  GCN: can be represented as SpMM
  GraphSage with flexible non-sum aggregation – not SpMM
  GIN with edge embedding – not SpMM
  PNA with multiple aggregation – not SpMM
  GAT with attention – not SpMM

## Slide 40: Feature 2 – Flexible

## Slide 41: Feature 3 – Standard PyTorch API
Create a fully parameterized GNN model using native PyTorch Geometric layers
Behaves as a standard nn.Module
  Zero gap from training to deployment

## Slide 42: Feature 3 – Standard PyTorch API (cont.)
(SW)
Model and layer definition
(HW)
HLS code generation and deployment on FPGA

## Slide 43: A Working Example using GNNBuilder
A minimum working example with:
GNN model definition
Training (omitted)
Code generation
Testbench generation
Synthesis and implementation

## Slide 44: Underneath of GNNBuilder – Templates
Pre-defined static array size
Define fixed-point data precision
Used for latency estimation
(can be omitted in deployment)
Linear layer parallelism
(can be decided by DSE later)

## Slide 45: Design Space Exploration (DSE)
How can I predict a given model’s resource usage and latency?
Analytical Model
  Look at HLS code and calculate a rough estimate of clock cycles and resources
  Failed: Too much complexity in HLS synthesis, mapping, and dynamic runtime
ML-based Model
  Use random forest on a dataset of 400 randomly sampled model designs + configurations
  Success!

## Slide 46: DSE Results – Analytical v.s. Analytical + ML

## Slide 47: DSE Results – ML based

## Slide 48: Implementation Results

## Slide 49: Implementation Results (cont.)
GNNBuilder is 6 faster than CPU/GPU at batch size 1

## Slide 50: GNNBuilder Limitations and Future Work
FlowGNN is 3 – 400 GPU speed up, GNNBuilder maxed out at 3
Core Issues
  No dataflow or steaming optimizations
    Simple HW implementation requires many unnecessary buffers and data copying
  No node-level parallelism
    Each node is evaluated sequentially, nodes are not processed in parallel
    Parallelism only exists in linear layers
Solutions
  Refactor HLS design using #pragma dataflow inside GNN conv layers
  Integrate node-level parallelism ideas from FlowGNN
Will open source soon!

## Slide 51: Edge-MoE – A multi-task vision transformer
LightningSim: Fast and Accurate Trace-Based Simulation for High-Level Synthesis
FlowGNN: A generic Graph Neural Network (GNN) accelerator on FPGA
GNNBuilder: An automated GNN accelerator generator
Architectures
EDA Tools
Edge-MoE: Multi-task Vision Transformer (HW)
DGNN-Booster: A Generic FPGA Accelerator Framework For Dynamic Graph Neural Network Inference
INR-Arch: A Dataflow Architecture and Compiler for Arbitrary-Order Gradient Computations

## Slide 52: Single-Task Learning (STL) for Multi-tasking
Original Video

## Slide 53: Multi-Task Learning (MTL) for Multi-tasking
Original Video

## Slide 54: Vision Transformer (ViT)
Original Video
Patches
Attention
MLP
Attention
MLP
…
Vision transformer Encoder
What about ViT for multi-tasking?

## Slide 55: Challenges of MTL + ViT
Original Video
Patches
Attention
MLP
Attention
MLP
…
Vision transformer Encoder

## Slide 56: STL v.s. MTL
Running a single task can only activate one backbone
Usually lower accuracy comparing to MTL
Higher accuracy comparing to STL
Running only one task needs to activate the entire shared backbone

## Slide 57: STL v.s. MTL
Running a single task can only activate one backbone
Usually lower accuracy comparing to MTL
Higher accuracy comparing to STL
Running only one task needs to activate the entire shared backbone

## Slide 58: STL v.s. MTL
Use Mixture-of-Expert (MoE):
dynamically select a sub-model
Edge-MoE
M3ViT

## Slide 59: M3ViT: MTL + ViT + MoE
Original Video
Patches
Attention
MLP

## Slide 60: M3ViT: MTL + ViT + MoE
Original Video
Patches
Attention
MoE
…
Expert 1
Expert 2
Expert 3
Expert 4
Expert N

## Slide 61: M3ViT: MTL + ViT + MoE
Original Video
Patches
Attention
MoE
…
Expert 1
Expert 2
Expert 3
Expert 4
Expert N
Router
Task B
Router
Task A

## Slide 62: M3ViT: MTL + ViT + MoE
Original Video
Patches
Attention
MoE
…
Expert 1
Expert 2
Expert 3
Expert 4
Expert N
Router
Task B
Router
Task A
Each task only select k out of N experts
Task-level sparsity saves a lot of memory and computation

## Slide 63: STL v.s. MTL. v.s. M3ViT

## Slide 64: M3ViT: MTL + ViT + MoE
Algorithm guy is happy now:
  MoE disentangles the parameter spaces and automatically avoids different tasks’ training conflict
Hardware guy is also happy:
  Load the required experts only – memory efficient
But… there are still challenges
Each task only select k out of N experts
…
Expert 1
Expert 2
Expert 3
Expert 4
Expert N
Router
Task B
Router
Task A

## Slide 65: MTL + ViT + MoE Challenge on Hardware
Load expert 1 and 4
Evict expert 1 and 4, load expert 2 and 8
Evict expert 2 and 8, load expert 4 and 6
…
Large data loading overhead!
Original Video
Patches
4
6
5
1
3
4
1
2
5
4
5
8
8
1
7
3
1
4
3
6
7
2
5
4
3
1
7
6
2
2
9
2
Patches even within the same task will select different experts…

## Slide 66: MTL + ViT + MoE + FPGA
Original Video
Patches
4
6
5
1
3
4
1
2
5
4
5
8
8
1
7
3
1
4
3
6
7
2
5
4
3
1
7
6
2
2
9
2
Solution:
Patch Reordering!

## Slide 67: MTL + ViT + MoE + FPGA
Original Video
Patches
4
6
5
1
3
4
1
2
5
4
5
8
8
1
7
3
1
4
3
6
7
2
5
4
3
1
7
6
2
2
9
2
Load expert
1
Compute patch 1, 5, 7, 10, 13

## Slide 68: MTL + ViT + MoE + FPGA
Original Video
Patches
4
6
5
1
3
4
1
2
5
4
5
8
8
1
7
3
1
4
3
6
7
2
5
4
3
1
7
6
2
2
9
2
Load expert
2
Compute patch 2, 5, 9, 11, 16
Load expert
1
Compute patch 1, 5, 7, 10, 13
…
A Patch is much smaller than an Expert

## Slide 69: MTL + ViT + MoE + FPGA Evaluation
On PASCAL-Context (simulated FPGA results)
Methods | FLOPS ↓ | Energy↓ | MTL  ↑ | Norm | H. Parts | Sal. | Edge | Seg
MTL-Baseline | 167 | 1.029 | 0 | 14.9 | 58.6 | 65.1 | 69.2 | 63.8
MTAN | 212 | 5.306 | +0.47 | 14.8 | 58.9 | 65.4 | 69.6 | 63.7
Cross-Stitch | 647 | 6.001 | +3.46 | 13.9 | 60.6 | 66.8 | 69.9 | 66.1
NDDR-CNN | 747 | 5.034 | +3.25 | 13.9 | 60.5 | 66.8 | 69.8 | 65.4
MTL ViT | 83 | 3.062 | +1.09 | 15.5 | 58.7 | 64.9 | 68.8 | 70.7
M2ViT (+MoE) | 84 | 7.446 | +5.57 | 14.5 | 62.1 | 66.3 | 71.7 | 72.8
M3ViT (+Codesign) | 84 | 0.690 | +5.57 | 14.5 | 62.1 | 66.3 | 71.7 | 72.8

## Slide 70: MTL + ViT + MoE + FPGA Evaluation
ViT beats ResNet
Methods | FLOPS ↓ | Energy↓ | MTL  ↑ | Norm | H. Parts | Sal. | Edge | Seg
MTL-Baseline | 167 | 1.029 | 0 | 14.9 | 58.6 | 65.1 | 69.2 | 63.8
MTAN | 212 | 5.306 | +0.47 | 14.8 | 58.9 | 65.4 | 69.6 | 63.7
Cross-Stitch | 647 | 6.001 | +3.46 | 13.9 | 60.6 | 66.8 | 69.9 | 66.1
NDDR-CNN | 747 | 5.034 | +3.25 | 13.9 | 60.5 | 66.8 | 69.8 | 65.4
MTL ViT | 83 | 3.062 | +1.09 | 15.5 | 58.7 | 64.9 | 68.8 | 70.7
M2ViT (+MoE) | 84 | 7.446 | +5.57 | 14.5 | 62.1 | 66.3 | 71.7 | 72.8
M3ViT (+Codesign) | 84 | 0.690 | +5.57 | 14.5 | 62.1 | 66.3 | 71.7 | 72.8

## Slide 71: MTL + ViT + MoE + FPGA Evaluation
ViT beats ResNet
MoE beats ViT only
Methods | FLOPS ↓ | Energy↓ | MTL  ↑ | Norm | H. Parts | Sal. | Edge | Seg
MTL-Baseline | 167 | 1.029 | 0 | 14.9 | 58.6 | 65.1 | 69.2 | 63.8
MTAN | 212 | 5.306 | +0.47 | 14.8 | 58.9 | 65.4 | 69.6 | 63.7
Cross-Stitch | 647 | 6.001 | +3.46 | 13.9 | 60.6 | 66.8 | 69.9 | 66.1
NDDR-CNN | 747 | 5.034 | +3.25 | 13.9 | 60.5 | 66.8 | 69.8 | 65.4
MTL ViT | 83 | 3.062 | +1.09 | 15.5 | 58.7 | 64.9 | 68.8 | 70.7
M2ViT (+MoE) | 84 | 7.446 | +5.57 | 14.5 | 62.1 | 66.3 | 71.7 | 72.8
M3ViT (+Codesign) | 84 | 0.690 | +5.57 | 14.5 | 62.1 | 66.3 | 71.7 | 72.8

## Slide 72: MTL + ViT + MoE + FPGA Evaluation
Methods | FLOPS ↓ | Energy↓ | MTL  ↑ | Norm | H. Parts | Sal. | Edge | Seg
MTL-Baseline | 167 | 1.029 | 0 | 14.9 | 58.6 | 65.1 | 69.2 | 63.8
MTAN | 212 | 5.306 | +0.47 | 14.8 | 58.9 | 65.4 | 69.6 | 63.7
Cross-Stitch | 647 | 6.001 | +3.46 | 13.9 | 60.6 | 66.8 | 69.9 | 66.1
NDDR-CNN | 747 | 5.034 | +3.25 | 13.9 | 60.5 | 66.8 | 69.8 | 65.4
MTL ViT | 83 | 3.062 | +1.09 | 15.5 | 58.7 | 64.9 | 68.8 | 70.7
M2ViT (+MoE) | 84 | 7.446 | +5.57 | 14.5 | 62.1 | 66.3 | 71.7 | 72.8
M3ViT (+Codesign) | 84 | 0.690 | +5.57 | 14.5 | 62.1 | 66.3 | 71.7 | 72.8
Energy
Accuracy
Speed
ViT beats ResNet
MoE beats ViT only
ViT + MoE + Co-design is the king

## Slide 73: M3ViT: Not Done Yet!
M3ViT is a big success (so far)
Still many challenges to implement on FPGA
  Heavy softmax operations inside attention
  Unfavorable GELU (Gaussian Error Linear Uni) activation
  Quadratic complexity of attention operation
  Limited hardware resource but many repeated computation
But we solved them all!

## Slide 74: Approximation for Softmax
Even for small values of and , exp(·) values can be too large and exceed fixed-point representations
Softmax Calculation:
Good feature: numerator and denominator can be shifted by the same value
So exp(·) values don’t grow too large

## Slide 75: Approximation for Softmax
Challenge: deciding the shift value of b is not trivial
Question: there are multiple exp() in the denominator; shall we go through all of them to decide a single b?
Two-pass: first decide b, then calculate denominator

## Slide 76: Approximation for Softmax
Two-pass: first decide b, then calculate denominator
One-pass is enough!

## Slide 77: Approximation for GELU (Gaussian Error Linear Units)
Difference between GELU and ReLU is symmetric about zero
Key idea: Use ReLU to compute GELU + delta

## Slide 78: M3ViT Evaluation on-FPGA
Measured on-FPGA (ZCU 102) with correct functionality: ~28.9 fps
Architecture | Latency (ms) (Speedup) | Hardware Resource |  |  |  | Sem. Seg. | Depth est. | Multi-task acc.
 |  | BRAM | DSP | LUT | FF | (mIoU↑) | (RMSE↓) | 
Baseline without proposed techniques | 650.3 (1.00x) | 84.6% | 65.9% | 60.8% | 46.9% | 63.81 | 0.0373 | +0.58%
+ Expert-by-expert reordering | 433.4 (1.5x) | 84.3% | 65.9% | 59.0% | 45.4% | 63.81 | 0.0373 | +0.58%
+Single-pass softmax with dynamic bias | 353.4 (1.84x) | 84.0% | 67.9% | 59.0% | 45.7% | 63.81 | 0.0373 | +0.58%
+Accurate, low-cost GELU | 212.9 (3.05x) | 64.1% | 63.0% | 45.5% | 34.9% | 63.84 | 0.0372 | +0.67%
+Unified linear layer module | 104.3 (6.23x) | 47.5% | 57.3% | 44.1% | 27.0% | 63.84 | 0.0372 | +0.67%
+Attention reordering | 34.6 (18.79x) | 48.1% | 61.6% | 46.5% | 27.5% | 63.84 | 0.0372 | +0.67%
Software baseline accuracy (PyTorch) |  |  |  |  |  | 63.95 | 0.0372 | +0.76%

## Slide 79: M3ViT Evaluation on-FPGA
Up to 10× after optimizations
5.70× and 2.65× better energy efficiency than CPU and GPU
Generally applicable to transformers

## Slide 80: M3ViT : On-board Results

## Slide 81: LightningSim – A fast and accurate HLS simulator
LightningSim: Fast and Accurate Trace-Based Simulation for High-Level Synthesis
FlowGNN: A generic Graph Neural Network (GNN) accelerator on FPGA
GNNBuilder: An automated GNN accelerator generator
Architectures
EDA Tools
Edge-MoE: Multi-task Vision Transformer (HW)
DGNN-Booster: A Generic FPGA Accelerator Framework For Dynamic Graph Neural Network Inference
INR-Arch: A Dataflow Architecture and Compiler for Arbitrary-Order Gradient Computations

## Slide 82: Simulation of HLS Designs
C Simulation
HLS Synthesis
C/RTL Co-sim
Speed
Accuracy

## Slide 83: Simulation of HLS Designs
C Simulation
C/RTL Co-sim
LightningSim
Not a tradeoff but with advantages of both sides
Speed
Accuracy

## Slide 84: What Can LightningSim Do?
Speed | Fastest | Slowest | Fast
Cycle-level simulation | ✘ | ✔ | ✔
Functionality verification | C-level | RTL-level | C + LLVM-level
Incremental stall analysis | ✘ | ✘ | ✔
Suggest fastest FIFO depths | ✘ | ✘ | ✔
C Simulation
LightningSim
C/RTL Co-sim

## Slide 85: Prior Work
FLASH: Fast, Parallel, and Accurate Simulator for HLS
  Choi et al. (TCAD 2020)
FastSim: A Fast Simulation Framework for High-Level Synthesis
  Abderehman et al. (TCAD 2022)
HLS
C/C++
RTL Generation
Static Timing Info.
RTL
code
C/RTL cosim
HLS synthesis
Scheduling and Binding
LLVM IR
Bitcode
Front-end
Compilation
FastSim
Flash
Starts after scheduling or RTL generation
Do we really need all these information to get started?

## Slide 86: Key Insights
A lot of information is already known at LLVM level
  Xxxxx
We process these info first and then combine scheduling info later
HLS
C/C++
RTL Generation
Static Timing Info.
RTL
code
C/RTL cosim
HLS synthesis
Flash
Scheduling and Binding
LLVM IR
Bitcode
Front-end
Compilation
FastSim
LightningSim
Starts simultaneously with scheduling
No RTL code required

## Slide 87: Our Approach
Map HLS scheduling information onto LLVM IR execution
Decoupled two steps:
  LLVM IR execution trace generation
  Trace analysis
HLS
C/C++
RTL Generation
Static Timing Info.
RTL
code
C/RTL cosim
HLS synthesis
Flash
Scheduling and Binding
LLVM IR
Bitcode
Front-end
Compilation
FastSim
1
2
LightningSim
Trace generation
Trace analysis
1
2
  Incremental simulation (e.g., stall and FIFO depth) without full simulation (as in co-sim)

## Slide 88: LightningSim Workflow
HLS Synthesis
LightningSim⚡
IR Trace Generation
❶
IR Trace Analysis
❷
(A) Make LLVM IR executable
Execute modified IR and dump a trace
(B) Make LLVM IR traceable
(C) Trace parsing
Non-pipelined non-dataflow basic blocks
Dataflow basic blocks
(D) Resolving dynamic schedule
(E) Calculating stalls
(F) Modeling AXI interfaces
LLVM IR
bitcode
Static
scheduling
information
Change
FIFO depth
Re-compute stalls
without re-simulating
(unlike current HLS
or simulation tools)
Dumped Trace
Decoupled
two
stages

## Slide 89: LightningSim Workflow
HLS Synthesis
LightningSim⚡
IR Trace Generation
❶
IR Trace Analysis
❷
(A) Make LLVM IR executable
Execute modified IR and dump a trace
(B) Make LLVM IR traceable
(C) Trace parsing
Non-pipelined non-dataflow basic blocks
Dataflow basic blocks
(D) Resolving dynamic schedule
(E) Calculating stalls
(F) Modeling AXI interfaces
LLVM IR
bitcode
Static
scheduling
information
Change
FIFO depth
Re-compute stalls
without re-simulating
(unlike current HLS
or simulation tools)
Dumped Trace
Decoupled
two
stages

## Slide 90: Trace Generation
HLS generated LLVM IR
Trace of LLVM basic blocks
BB1
BB2
BB4
BB1
BB3
BB4
BB1
BB3
BB4
time
(a) Generate undefined functions on-the-fly
(b) Insert helper code into IR for tracing
LightningSim modified LLVM IR
Compile and Run!

## Slide 91: LightningSim Workflow
HLS Synthesis
LightningSim⚡
IR Trace Generation
❶
IR Trace Analysis
❷
(A) Make LLVM IR executable
Execute modified IR and dump a trace
(B) Make LLVM IR traceable
(C) Trace parsing
Non-pipelined non-dataflow basic blocks
Dataflow basic blocks
(D) Resolving dynamic schedule
(E) Calculating stalls
(F) Modeling AXI interfaces
LLVM IR
bitcode
Static
scheduling
information
Change
FIFO depth
Re-compute stalls
without re-simulating
(unlike current HLS
or simulation tools)
Dumped Trace

## Slide 92: Trace Resolution
Examine the trace of basic blocks for each function call in the hierarchy
Map the HLS static scheduling data (FSM states) into a dynamic schedule
Trace of LLVM basic blocks
Instruction
Static Stage
fifo_read
br
subcall1
br
subcall2
mul
br
1
2
3
4
5
br
BB1
BB2
BB3
BB4
Basic Block
Static Stage
add
Dynamic Stage
1
1
2
3
2
3
4
4
5
1
6
5
7
3
8
4
BB1
BB2
BB4
BB1
BB3
BB4
Time
Time
(D) Schedule
Resolution

## Slide 93: LightningSim Evaluation
99.9%-accurate on cycle counts comparing to C/RTL co-sim
100% accurate for 26 out of 33 cases
5.6–95.9× speedup over cosim (usually highest for larger designs)
  For FlowGNN GIN, cosim takes 1h 10m; LightningSim takes 44 seconds
Finishes faster than HLS synthesis in 13 of 33 cases

## Slide 94: Performance Results
LightningSim finishes
HLS Synthesis finishes
For many cases, LightningSim finishes earlier than HLS synthesis!

## Slide 95: Our ROAD4NN – Future?
Architectures
EDA Tools
LightningSim
FlowGNN
GNNBuilder
Edge-MoE
DGNN-Booster
INR-Arch
The Best Way to Predict the Future is to Create it.
– P. Drucker & A. Lincoln

## Slide 96: Contact
Software/Hardware Co-Design for Intelligence and Efficiency
  Email: callie.hao@ece.gatech.edu
  Homepage: http://sharclab.ece.gatech.edu